# Sector Functionality Tests

- Visual inspection

  - Inspection of each HS and extender, documentation of defects using photographs

  - Pictures available on https://twiki.cern.ch/twiki/bin/view/AliceSPD/WebHome

- Electrical test of the extenders

  - Document shorts or other defects

- Power and configure MCM and pixel chips (sensor bias at 2V)

  - Measure MCM and bus currents

  - Are all configuration files available?

  - Document HS that show difficulties during configuration

- Sensor leakage current

  - Measure I-V up to 50V

  - Are some HS light-sensitive?

  - Does a HS need “training”?

  - Which HS show soft breakdown at what voltage?

  - Which HS cannot be operated at 50V?

- Temperature

  - Document pt1000 temperatures for all HS

  - Take pictures with thermal camera

  - Pictures available on https://twiki.cern.ch/twiki/bin/view/AliceSPD/WebHome

- Noisy pixel scan

  - Identify noisy pixels and mask them

  - Save noisy pixel information

- Min. threshold scan

  - Scan pre_vth and note min. values

- Uniformity matrix

  - Find optimum delay and document it, note strobe length

  - Check for data inconsistencies and document them

  - Document dead pixels and test columns

  - Any problems during readout?

- Source test

  - Use Sr90 source, scan across the sector

  - No. of triggers ?

- FO test

  - Measure FO efficiency for each chip